## Slide 1
Welcome!
Fundamentals of Site Plan Reading

## Slide 2: CLEAR Program Areas
Water
Geospatial Tools & Training
STEM Education & Local Conservation
Land Use & Climate Resiliency
Website: clear.uconn.edu
David Dicksson – David.Dickson@uconn.edu
Renata Bertotti – rbdmd25@gmail.com
Notes: We at CLEAR work in four program areas – water, LU and Climate Resiliency which I am a part of, Geospatial tools and training and STEM Education and local conservation. You can find more of each of these program areas and great things we do by visiting the Clear website.

## Slide 3
Fundamentals of Reading Plans
Land Use Academy
Plans = engineered drawings showing existing conditions and proposed development
Scale, Measuring Distances and Topography
Reading A Site Plan (Great Neck School, Waterford, CT)
We will Cover:
Notes: Tonight we will talk about reading plans:
So, if you are comfortable with doing so, by raise of hands, I would be interested to see how many of you either work or have retired out of a profession that has nothing to do with reading of site plans?
Great! Tonight’s agenda will be to talk about the
Difference Between Plans and Map
Scale, Measuring Distances and Topography
Reading A Site Plan
We will look at the actual plan for The Great Neck school in Waterford CT and if we have the time, we will do a fun exercise called ‘follow the water’

## Slide 4: An Awesome Responsibility
CGS Sec. 8-4c
Land Use Commissions make decisions that affect a community’s quality of life for generations, where investment takes place and an individual’s or business’s financial well being.
Notes: If you attended the Part 1 of training, you saw this slide and heard me talk about this:
– the reason that you may be here:
I suspect that many of you are here because this training is now required by the general statutes / meaning, the members of planning, zoning, and the ZBA need to get 4 hours of training by January 1, 2024, and this session today, we believe, can count towards 1.5 credits of the required 4 credits – I hope that most of you are here because you want to learn.
We at CLEAR have provided the training for at least two decades now because we know how important what you do is.

## Slide 5: An Awesome Responsibility
Notes: That way you will avoid approving things like this…
Being able to understand and read plans helps you avoid mistakes like this

## Slide 6: An Awesome Responsibility
Notes: Or like this

## Slide 7: Maps, Plans...What’s the Difference?
Maps show physical features of the natural or built environment at established scale and orientation.
Plans are engineered drawings made to scale showing existing physical features of a site and proposed changes to accommodate development.

## Slide 8: Subdivision Plans
Plan to divide one lot into 3 or more
Town regulates lot size, frontage,
Setbacks, road construction, etc
Planning Commission’s Role
Once approved, each home builder submits construction documents for building permit; once complete a CO is issued (Certificate of Occupancy)

## Slide 9: Site Plans
Zoning Commission for administrative review to see if it meets regulations
If it doesn’t meet regulations, must go to Zoning Board of Appeals for variance
ZBA can only grant variances if there is a hardship with the ‘land’

## Slide 10
What Does This Map/Plan Tell Me?
Notes: Whether it is a map or a plan – it really is all about information. And once you know how to interpret it, there is often tons of information you can find on them.

## Slide 11
Maps are 2-dimensional representations of complex landscapes…at a specific point in time!
A map may not represent what is on the ground
-Alford Korzybski
?

## Slide 12: What you see may look something like this
Notes: This is a typical set of site plans – this is the set for Great Neck School in Waterford CT and it has 42 separate drawings. A typical set like this can include a
Cover Sheet
Existing Conditions Plan
Demolition Plan
Utilities Plan
Site Plan
Drainage
Landscape Plan
Detail Sheets
E&S Control
Building Elevations
Floor Plans

## Slide 13: Typical Set of Plans May Contain:
Cover Sheet
Existing Conditions Plan
Demolition Plan
Utilities Plan
Site Plan
Landscape Plan
Detail Sheets
Drainage
E&S Control
Building Elevations
Floor Plans
Notes: This is a typical set of site plans – this is the set for Great Neck School in Waterford CT and it has 42 separate drawings. A typical set like this can include a
Cover Sheet
Existing Conditions Plan
Demolition Plan
Utilities Plan
Site Plan
Drainage
Landscape Plan
Detail Sheets
E&S Control
Building Elevations
Floor Plans

## Slide 14: What Is This Plan Telling Me?
Notes: So, if we take it apart and look at each individual sheet we will see all kinds of things:
Project data, open space, water features, Swimming pools, off site loading and parking and even a lot more if you look at symbols.
So once you take a plan set and take it apart, the information becomes much clearer.

## Slide 15: Help is on the Plans
Location Map
List of Drawings
Orientation
Title Block
Legend
Scale
Zoning Table
Notes
And More….

## Slide 16: Location Map
Notes: So, let’s look at some of this information step by step:
Location map – is exactly that – it is a map that shows a location of the site in relation to the rest of the community

## Slide 18
Orientation: North Arrow
North arrow can change on different plan sheets

## Slide 19
Map Orientation Matters…A Lot!
Notes: Map orientation matters and in any given plan set you may happen to have plan sheets with different orientation.
We will talk about this more in a moment but I wanted to bring to your attention this slide that we looked at just a moment ago – which – if you look closely
So, as you can see, understanding where north is very important. If you did not know that north was in this direction, you would expect this development to be here and thought that it was not built.

## Slide 20
Title Creation & Revision Dates Source
Cartography Road Mapville, CT
XYZ GROUP/ ABC ASSOCIATES
500 Longitude Boulevard Mapville, Connecticut 06001 860-555-5555
Information on who/what/when etc
Title Block

## Slide 21
Provide a guide to the symbols used
Legends

## Slide 22: Zoning Compliance Chart
Notes: The Set of plans should always include the zoning compliance table affirming the compliance with the zoning regulations:
This chart includes all kinds of helpful information you are looking for in your review
For example: You can see here in the required column what is required by the zoning regulations and then whether each of the proposed lots (in this instance it is a proposed subdivision) complies with the zoning regulations
For example required lot with in R-40 zone is 125 feet and each lot meets it

## Slide 23: Notes and Map References
Notes: You will also have notes and map references on plans. These are very helpful to understand what is going on and how the plans were developed. In this instance you can see that wetlands were field delineated by Robert Russo – meaning that the site has been surveyed and looked by a wetland scientist and that is how the wetland boundary was accurately located on set of plans. You can also see that the site is not in flood hazard area based on FEMA map that was last revised in 1995.
Easy way to add conditions without changing sheets—i.e. construction hours, Storm system Maintenance every quarter w/ report to town engineer

## Slide 24: Shows relative size of objects
Scale
35’
20’ !

## Slide 25: Scale Shows relative size of objects
Graphical Scale
Written Scale
1:12,000 (ratio)
1” = 1,000’ (equivalent)
Graphic scales are the most reliable!
Beware of Xerox Distortion
Notes: May 29, 2026
Land Use Academy
25

## Slide 26
Map Scale | Meaning
10 | 1 inch = 10 ft
20 | 1 inch = 20 ft
30 | 1 inch = 30 ft
40 | 1 inch = 40 ft
50 | 1 inch = 50 ft
60 | 1 inch = 60 ft
Measuring Distances
Engineering Scales
40 ft
240 ft
400 ft

## Slide 27
1”=40’
Measuring Distances
55’

## Slide 28
Notes: Bruce sent out a request to planners for example of bad plans and got this drawing from one of our local planners –
You can see how on this drawing the distance from the street is shown as 45 feet but the length of the building is 24 feet – Clearly this person has somewhat limited concept of scale. This is a good example of a drawing that probably should have a NTS note on it.

## Slide 29
Map Scale | Meaning
10 | 1 inch = 10 ft
20 | 1 inch = 20 ft
30 | 1 inch = 30 ft
40 | 1 inch = 40 ft
50 | 1 inch = 50 ft
60 | 1 inch = 60 ft
Measuring Distances
Engineering Scales
40 ft
240 ft
400 ft
Let’s measure!

## Slide 30: Topography
Contours: an imaginary line that connects points of equal elevation
Notes: Contours: an imaginary line that connects points of equal elevation
If you were to look at the contours on this hill you would see that they are in 50’ intervals and the tops of the hills are shown as spot elevations
So if you wanted to look at 200 foot elevation on a set of plans that showed contours you would see the spot elevations on the tops of the two hills there and there would be 200 foot contour there
an

## Slide 31: Topography
Contours: an imaginary line that connects points of equal elevation
Notes: Contours: an imaginary line that connects points of equal elevation
If you were to look at the contours on this hill you would see that they are in 50’ intervals and the tops of the hills are shown as spot elevations
So if you wanted to look at 200 foot elevation on a set of plans that showed contours you would see the spot elevations on the tops of the two hills there and there would be 200 foot contour there
an

## Slide 32
Cross-sections are sometimes used to represent 3-D objects in 2 dimensions.
Topography
Notes: May 29, 2026
Land Use Academy
32
Cross-sections are used to represent 3-Dimensional objects in 2 dimensions. If we were to put the cross section through the top of the two hills there and draw vertical lines connecting them to where the cross section intersects the contours we would get this 2 dimensional representation of the hill at that particular cross section.

## Slide 33: Topography
Contours always connect,
but not always within the map boundaries...
topography of 2 hills
This could be the edge of a presented map

## Slide 34: Topography
Slope direction is calculated perpendicular to the contour lines.
Water flows downhill...
...so the direction of flow is always perpendicular to the contour lines, since this is the steepest slope

## Slide 35
every 5th contour is an index contour shown in bold
contours far apart show a gentle slope
contours close together show a steep slope
a series of concentric contours ending in a small closed circle or oval shows a local hilltop
contours at a stream form a “V” that always points uphill
contours very close together show a cliff
a spot elevation is a point of known elevation used as a pt of reference for surveys.
green areas show forest cover;
white areas denote fields
a contour interval is the vertical distance b/w contours. 10’ on topos; 2-5’ on site plans
contour lines of a ridge are in a “U” that always points downhill

## Slide 36
Notes: So,
Let’s try to match the contours on the left to the profiles on the right side.
If you look at A and D – 6 and 3 – you can see that they look similar, but you can see contours close together – which means steeper hill in 6 and they further apart and flatter at the tops in 3 and you have gentler hills in figure D.

## Slide 37: Topography-Slope
Slope direction is calculated perpendicular to the contour lines.
... But how do you measure it?
Notes: Slope direction is calculated perpendicular to the contour lines.
But – how do you measure it?

## Slide 38: Slope
Percent Slope =
10 ft
20 ft
Change in Elevation
Distance
X
100
(10’ / 20’ ) X 100 =
50% slope
Notes: So if you have an elevation change of 10 feet over the distance of 20 feet to get to the slope, you would divide the elevation change 10 ‘ with distance of 20’ and multiply that with a 100 to get to the percent.

## Slide 39: Why is Slope Important?
If too Steep:
- potential erosion
- soil stability
- safety
10 ft
20 ft
Notes: If it is too steep you may have erosion and soil stability problem

## Slide 40: Why is Slope Important?
If too flat:
- storm water may not drain
- may flood
0 ft
20 ft
Notes: Why is it important – well if it is flat the you will get flooding because the water will not drain

## Slide 41: Too steep?
Notes: On the Commission you may have heard things such as – a driveway is proposed at 12% grade and the town engineer thinks that is too steep, or the subdivision road is proposed at 8% grade and the maximum allowed is 10% - or slope during the construction will be 3 to 1 and this type of erosion and control measure will be used, and in this other location the slope will be 2 to 1 so this other, reinforced, type of erosion control measure will be utilized…
So how steep is steep: A 15 percent grade is very steep. In fact it is so steep that most people would have a hard time walking up it. This is because the angle of the grade is such that it is almost like walking up a flight of stairs. In fact if you were to put a15 percent grade in front of a building it would be the equivalent of having a staircase with 12 steps.
This will give you an idea of what a steep slope really is – this is a slope of 40-45 degrees which when you are looking at on a graph may not look as that much. But when you look at it in real life it is very bery steep – this is Tuckerman’s ravine on Mt Washington where many people like to go to ski.

## Slide 42
Site Plan Reading
FHA Pharmacy
Survey
Layout Plan
Grading Plan
Utility S&E Control
Elevation
Planting Plan
Details
Let’s go through this set of plans, page by page.

## Slide 43: Plan Reading
who? what? where? when?
TAKE IT APART &
START ASKING QUESTIONS
03/12/05
Are they qualified?
What’s the project name?
Where is it?
Where’s north?
What’s the scale?
What kind of plan?
Who prepared the plan?
What’s it all Mean?
When drawn?

## Slide 44: Plan Reading
03/12/05

## Slide 45: Plan Reading
03/12/05
Steeper
More Level
Question: Where’s the steepest and the flattest areas?

## Slide 46: Plan Reading
03/12/05
Steeper
More Level
HP
LP
Question: Where are the high and low points?

## Slide 47: Plan Reading
03/12/05
Question: What direction does the water flow on the road?
HP

## Slide 48: Plan Reading Traffic Circulation

## Slide 49: Plan Reading
What’s the lot size?
Regulations: 1 ac.
Lot is 1.34 ac.
ask questions ……

## Slide 50: Plan Reading
Is that enough frontage?
Regulations: 100’ min.
122’
40
Double Frontage

## Slide 51: Plan Reading
Is the building within setbacks?
Regulations: 40’ front
10’ side
27’
46’
131’

## Slide 52: Plan Reading
How many parking spaces?
9
4
5
8
8
2
Regulations: 41 + 2
34 + 2

## Slide 53: Plan Reading
What’s the distance from the intersection?
Regulations: 75’
62’
108’

## Slide 54: Plan Reading

## Slide 55
Site Plan Review – Cut and Fill
Question: Why should you be concerned with the amount of cut and fill?
CUT
FILL

## Slide 56
Plan Reading
focus in

## Slide 57
Site Plan Review
Grading Plan
Original grade is shown as dashed line 610
Grade changes MUST be within property boundary
Proposed Grade is shown as a solid line and as 610

## Slide 58
Site Plan Review
How does water flows across the front parking lot

## Slide 59
Site Plan Review

## Slide 60
Site Plan Review
Stormwater System

## Slide 61
Site Plan Review
Stormwater System
TF 609.10
EO 600.50
BP 559
Question: Any concerns?
System Schematic

## Slide 62: Landscaping/Planting Plan
Notes: Let’s now look at landscaping plan
On the bottom you can see the plant locator as a box which has a lower part of the box and the lower part of the box. Top portion of a box is where you will see the quantity of plants that are supposed to be planted in a particular location and the lower part of the box is where you will see the plant key or the type of plants. In this case it would be one green mountain sugar maple planted in a particular location where this symbol is shown.

## Slide 63: Landscaping/Planting Plan
Notes: Any development of any size is likely to have a plant list, and you can see here that there is a key that tells you what kinds of plant it is MA which we had before which is a sugar maple or JP which is dwarf Japanese garden juniper, in this case there is 107 of them, they are to be planted at 18”-24” spread and planted at 4’ on center

## Slide 64: Landscaping/Planting Plan
Notes: If we take a closer look at Landscaping Plan we will see that there are 4 PS here. That is 4 Kwansan Flowering Cherry / there are 24 of them total on the site, only 4 of them in this particular location /
And PC which is Flowering Pear / 9 of them total on the site, but only 1 of them in this particular location

## Slide 65: Landscaping/Planting Plan
Notes: Generally, there is always a lot of notes on the planting plan. For example, the final plant locations shall be coordinated in the field so that no tree is planted within approximately 6 feet of any underground utility new or existing which is a good idea.

## Slide 66
Site Plan Review
Utilities
Utility connections

## Slide 67
Site Plan Review
Sediment and Erosion Control
Construction Activity

## Slide 68
Site Plan Review
Details S&E

## Slide 69
Site Plan Review
Details

## Slide 70
Site Plan Review
Construction Activity

## Slide 71
Site Plan Review
Details S&E
Silt Fence
Anti-Tracking Pad
Hay-Bales

## Slide 73: And now—It’s your turn
Great Neck School, Waterford, CT

## Slide 74
Dry Swale L-1.5
Notes: If you look on the plan sheet L-1.5
In this proposed development – the Great Neck School in Waterford – there are four dry swales located adjacent to the driveway and to the parking lot

## Slide 75
Notes: This is the closer look at one of the dry swales
You can see that in the middle of the dry swale there is a berm with the elevation 88 feet, and the elevation on each side of that berm is 87 feet.
The purpose of the berm is to slow the water down that is headed to the yard drain – and I will show you that in a moment - and to allow the water to percolate through the soil.
The lawn drain will put any excess precipitation that has not percolated that falls onto the site through the stormwater system.
here at 85.25

## Slide 77
Flush Concrete Curb L-1.3
Notes: The flush concrete curb you can see on sheet L-1.3 and it is indicated by the bold dashed line highlighted for you in the red there

## Slide 78
Notes: If you look at the legend, this is what the symbol in the legend looks like
It is this dotted line for flush curb which is on the site adjacent to the stone erosion control stirp
The purpose the erosion control strip is to slow the water down as it sheet flows off the driveway into the dry swale
In addition, on this section, you can also see a 6’ taper along the curb which is the transition from essentially no curb (or flush curb) to regular (raised) curb at the driveway.
And the note as to where you can find the details as to how the flush concrete should be built is on Plan sheet L -1.13 drawing number 13.

## Slide 80
6’ Taper
Notes: So, this is what those things look like in real life
Circled in red is flush curb – which is at the same elevation as pavement of the road, then you have the taper leading to the raised curb,

## Slide 81
Notes: Here is another view of the flush curb with the stone erosion control strip

## Slide 82
Turf Pavers L-1.3
Notes: Next we will look at Turf Pavers which are shown on the plan sheet L-1.3
They are a little difficult to see but they are here, adjacent to the walkway to the school

## Slide 83
Notes: Here is the Closer look at turf pavers - they are represented in the legend with this polka-dot pattern symbol
And adjacent to the concrete walkway
Their purpose in this location is to allow vehicles to occasionally get behind the school without tearing up the lawn or sinking into the mud if it is particularly wet time. They also, as LID practice, and green infrastructure should, allow precipitation to percolate into the soil

## Slide 84
Notes: This is what turf pavers look like in real life.

## Slide 85
Wet Swale L-1.5
Notes: And lastly, this is what wet swale looks like on a site plan – plan sheet L-1.5
And you can see it there circled

## Slide 86
Drainage Plan Sheet C-2.0A
Grading Plan Sheet L-1.5
Notes: You can see the wet swale and the adjacent rip-rap armored berm on the Grading Plan Sheet L-1.5 and Drainage Plan Sheet C-2.0A
On the plans there are instructions as to how the wet swale is to be constructed –
You may notice that wet swale and rip-rap armored berm look different on a grading sheet and on a drainage sheet. So – which one should you believe / look at?
In these situations what you do is - you look for plan references – and in this instance at the drainage plan there is a detail plan reference (Drawing #7 on Plan Sheet C-4.2) and if you have something that is confusing like this, you then go and look at the detail drawing which will show the correct way for this peace of infrastructure to be built.

## Slide 87
Notes: This is what wet swale looks in real life. You can see the wet swale back in smaller red circle. The wet swale holds water most of the time unless we have a particularly dry year. Rip_rap armored berm slows the water down as it comes and gradually directs it towards to wet swale.

## Slide 88: Questions
What is the first floor elevation at the southwest corner of the existing school? Sheet 1
When were the plans last revised? Sheet 1
What is the required setback from the road? Sheet 1
How many lawn drains are the in the swales adjacent to the parking lots? L-1.5
What is the elevation of the bottom of the wet swale? L-1.5
What is the approximate elevation of wetland flag #21? C-2.0A
What is the distance from catch basin #1 (CB01) to catch basin#2 (CB02)? C-2.0A
On which detail sheet would you find the details of the basketball court? L-1.3
What material is sidewalk at the entrance to the school made from? L-1.3
What type of trees are planted along Great Neck Rd. L-1.9
What type of plants are planted in the wet swale? L-1.9
Follow the rain

## Slide 89: #1 FF Elevation of Existing School

## Slide 90: #2 Last Revision

## Slide 91: #3 Setback from Great Neck Rd

## Slide 92: #3 Setback from Goshen Rd

## Slide 93: #4--How Many Lawn Drains

## Slide 94: #5 Elevation at Bottom of Wet Swale

## Slide 95: #6 Elevation of Wetlands Flag #21

## Slide 96: #7 Distance from CB01 to CB02
90’

## Slide 97: #8 Basketball Court Detail Sheet

## Slide 98: #9 Sidewalk Treatment at Entrance

## Slide 99: #10 Trees Along Great Neck Rd.

## Slide 100: #11 Plants in Wet Swale